YC6J245-30(J61LA)柴油机零件图册

Parts Catalogue of YC6J245-30(J61LA) Diesel Engine

广西玉柴机器股份有限公司

Guangxi Yuchai Machinery Co., Ltd.

前   言

Foreword

感谢您选用广西玉柴机器股份有限公司的产品，并感谢您阅读《YC6J-30(J61LA)柴油机零件图册》！

Thanks for using Yuchai engine and reading the “Parts Catalogue of YC6J-30(J61LA) Diesel Engine”!

玉柴的服务宗旨是：“倾我所有、尽我所能、竭诚用户、诚信天下”,为了更好地履行玉柴的服务宗旨，我们编印了《YC6J-30(J61LA)柴油机零件图册》，希望本图册可以让用户更好地认识了解玉柴产品的结构与配置，方便用户使用、维修和购置零配件。

With the aim to fulfill our company service tenet, i.e. “striving all out to serve the customers, spending full sincerity to confidence the world”, we compiled and printed this “Parts Catalogue of YC6J-30(J61LA) Diesel Engine”. We hope this “Parts Catalogue of YC6J-30(J61LA) Diesel Engine” will help you to understand the structure and configuration of Yuchai’s YC6J-30(J61LA) diesel engines, so to operate and maintain them easily.

本零件图册是根据相关生产图样、资料编制而成的。图册中列出了YC6J-30(J61LA)柴油机的全部零部件目录。

This “Parts Catalogue of YC6J-30(J61LA) Diesel Engine” is compiled by basing on the production samples and technical documents, and covers the engine model of YC6J-30(J61LA) diesel engine.

随着产品的不断改进提高和用户不断提出新的要求，《YC6J-30(J61LA)柴油机零件图册》中的有关内容将会有不同程度的变更，玉柴保留在不预先通知的情况下进行修改的权利，具体配置情况应以当时产品技术文件为依据。

As production improvements and consumer’s requirements are constantly brought up, the content of this “Parts Catalogue of YC6J-30(J61LA) Diesel Engine” must be changed at a certain extent, which Yuchai reserves the right to modify without formal notification beforehand. The engine’s idiographic configuration is according to its technical documents.

本零件图册编写不足之处在所难免，敬请多多指教，使之渐臻完善。谢谢！

Deficiencies may appear in this “Part Catalogue of YC6J-30(J61LA) Diesel Engine”, and your comments and suggestions are appreciated honestly!

广西玉柴机器股份有限公司

Guangxi Yuchai Machinery Co. Ltd.

目    录  CONTENT

| 序号 Item | 图 号 Part No. | 名 称 | Parts Name | 页数 Page | 备注 Remark | 序号 Item | 图 号 Parts No. | 名 称 | Parts Name | 页数 Name | 备注 Remark |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | J5600-1002000 | 气缸体总成 | Cylinder Block Assembly |  | 图Drawing | 17 | J5600-1104000 | 供给系管路总成 | Fuel Supply Lines Assembly |  | 图Drawing |
| 2 | J5600-1002200 | 齿轮室部件 | Gear Housing Parts |  | Drawing | 18 | J5600-1105000 | 柴油滤清器总成 | Fuel Filter Assembly |  | Drawing |
| 3 | J5600-1003000 | 气缸盖及气缸盖罩总成 | Cylinder Head & Cylinder Head Cover Assembly |  | Drawing | 19 | J5600-1111000 | 喷油泵总成 | Injection Pump Assembly |  | Drawing |
| 4 | J5600-1004000 | 活塞及连杆总成 | Piston & Connecting Rod Assembly |  | Drawing | 20 | J5600-1112000 | 喷油器总成 | Injector Assembly |  | Drawing |
| 5 | J5600-1005000 | 曲轴减振器总成 | Crankshaft Vibration Damper Assembly |  | Drawing | 21 | J5600-1118000 | 增压器总成 | Turbocharger Assembly |  | Drawing |
| 6 | J5600-1006000 | 凸轮轴总成 | Camshaft Assembly |  | Drawing | 22 | 631-1305000 | 放水开关总成 | Water Drain Cock Assembly |  | Drawing |
| 7 | J5600-1007000 | 配气机构总成 | Valve Train Mechanism Assembly |  | Drawing | 23 | J5600-1306000 | 调温器总成 | Thermostat Assembly |  | Drawing |
| 8 | J5600-1008100 | 进气管部件 | Intake Manifold Parts |  | Drawing | 24 | J5600-1307000 | 水泵总成 | Water Pump Assembly |  | Drawing |
| 9 | J5600-1008500 | 进气接管部件 | Air Intake Pipe Parts |  | Drawing | 25 | A3100-1308000 | 风扇部件 | Fan Parts |  | Drawing |
| 10 | J5600-1008200 | 排气管部件 | Exhaust Manifold Parts |  | Drawing | 26 | J5600-1600000 | 动力输出总成 | Power Output Assembly |  | Drawing |
| 11 | J5600-1008400 | 气管护罩部件 | Manifold Cover Assembly |  | Drawing | 27 | A3000-3407000 | 转向泵总成 | Steering Pump Assembly |  | Drawing |
| 12 | J5600-1009000 | 油底壳总成 | Oil Sump Assembly |  | Drawing | 28 | J6000-3509000 | 气制动空气压缩机总成 | Pneumatic Air Compressor Assembly |  | Drawing |
| 13 | J5600-1010000 | 机油集滤器总成 | Oil Strainer Assembly |  | Drawing | 29 | J5600-3701000 | 发电机总成 | Alternator Assembly |  | Drawing |
| 14 | J5600-1011000 | 机油泵总成 | Oil Pump Assembly |  | Drawing | 30 | A3206-3708000 | 起动机总成 | Starter Assembly |  | Drawing |
| 15 | A3100-1012000 | 机油滤清器总成 | Oil Filter Assembly |  | Drawing | 31 | 1532-3800000 | 仪表、感应器总成 | Sensors |  | Drawing |
| 16 | A3100-1013000A | 机油冷却器总成 | Oil Cooler Assembly |  | Drawing |  | J5600-3823000 | 控制系统总成 | Control System Assembly |  | Drawing |

EWP=Easy wear part　(易损件)

1图Drawing

1.  J5600-1002000  气缸体总成 Cylinder Block Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | J5600-1002370D | 惰齿轮润滑油管 | Idler gear lubrication pipe | 1 |  |
| 2 | Q/YC901-1C0810 | 铰接螺栓M8×1 | Articulated bolt M8× 1 | 1 |  |
| 3 | Q/YC149-8 | 复合式密封垫圈8 | Seal washer8 | 2 | 易损件 EWP |
| 4 | 150-1112012 | 螺栓 | Bolt | 1 |  |
| 5 | 150-1112011 | 垫圈 | Washer | 2 | 易损件 EWP |
| 6 | Q618B01 | 螺塞NPT1/8 | Screw plug NPT 1/8 | 1 |  |
| 7 | J5600-1002052 | 惰齿轮轴 | Idler gear shaft | 1 |  |
| 8 | Q61508 | 螺塞M8×1 | Screw plugM8× 1 | 1 |  |
| 9 | 6105QA-1002011 | 凸轮轴衬套 | Camshaft bushing | 1 |  |
| 10 | A3000-1002051 | 正时惰齿轮 | Timing idle gear | 1 |  |
| 11 | Q150B1055TF2 | 螺栓M10×55 | Bolt M10× 55 | 3 |  |
| 12 | A3100-1002054A | 正时惰齿轮挡板 | Timing idle gear plate | 1 |  |
| 13 | 6105Q-1002067 | 主油道密封塞 | Main oil gallery seal plug | 1 |  |
| 14 | YC208-B01800F | O形圈2.65×18 | O-ring 2.65× 18 | 1 | 易损件 EWP |
| 15 | L3000-1002011 | 凸轮轴衬套 | Camshaft bushing | 7 |  |
| 16 | A3000-1002063B | 气缸套封水圈 | Cylinder liner O ring | 6 | 易损件 EWP |
| 17 | A3000-1002063 | 气缸套封水圈 | Cylinder liner O ring | 6 | 易损件 EWP |
| 18 | J5600-1002106 | 气缸套 | Cylinder liner | 6 |  |
| 19 | J5600-1002114A | 气缸体 | Cylinder block | 1 |  |
| 20 | 6105Q-1014001 | 呼吸器垫片 | Breather spacer | 1 | 易损件 EWP |
| 21 | A7100-1319K-0 | 盖板 | Cover plate | 1 |  |
| 22 | Q1840816 | 螺栓M8×16 | Bolt M8× 16 | 2 |  |
| 23 | 6105Q-1002022 | 铝堵φ10×10 | Aluminum plug Φ10×10 | 2 |  |
| 24 | Q72230 | 塞片30 | Spacer 30 | 6 |  |
| 25 | A3100-1002103 | 凸轮轴端盖垫片 | Camshaft end cover gasket | 1 | 易损件 EWP |
| 26 | A3100-1002102 | 凸轮轴端盖 | Camshaft end cover | 1 |  |
| 27 | Q1840816 | 螺栓M8×16 | Bolt M8× 16 | 2 |  |
| 28 | 6105Q-1002069 | 后主油道堵塞 | Rear main oil galley plug | 1 |  |
| 29 | J5600-1002740 | 喷嘴焊接件 | Nozzle weldment | 6 |  |
| 30 | Q5220510 | 销5×10 | Pin 5×10 | 6 |  |
| 31 | 430-1002163 | 垫圈 | Washer | 6 |  |
| 32 | A3100-1002180 | 过油螺栓组件 | Bolt with oil hole (assembly) | 6 |  |
| 33 | J5600-1002161 | 机体加强板 | Block reinforced plate | 1 |  |
| 34 | Q150B0840TF2 | 螺栓M8×40 | Bolt M8× 40 | 15 |  |
| 35 | Q1841040TF2 | 螺栓M10×40 | Bolt M10×40 | 8 |  |
| 36 | Q218B0830TF2 | 螺钉M8×30 | Screw M8× 30 | 13 |  |
| 37 | A30-1002021 | 主轴承螺栓 | Main bearing bolt | 14 |  |
| 38 | A30-1002019 | 主轴承螺栓垫圈 | Main bearing bolt washer | 14 |  |
| 39 | A30-1002012 | 前主轴承盖 | Front main bearing cap | 1 |  |
| 40 | YC208-C02580F | O形圈3.55×25.8 | O-ring 3.55× 25.8 | 1 | 易损件 EWP |
| 41 | A30-1002014 | 主轴承盖 | Main bearing cap | 5 |  |
| 42 | A30-1002013 | 中间主轴承盖 | Medium main bearing cap | 1 |  |

2图Drawing

2.  J5600-1002200  齿轮室部件 Gear Housing Parts

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | Q1841070TF2 | 螺栓M10×70 | Bolt M10× 70 | 1 |  |
| 2 | G0100-1002401 | 张紧皮带轮 | Tension pulley | 1 | 选装件 Optional |
|  | A3200-1002045A | 张紧轮总成 | Tensioner assembly | 1 | 选装件 Optional |
| 3 | Q1840815 | 螺栓M8×15 | Bolt M8× 15 | 2 |  |
| 4 | Q/YC149-8 | 复合式密封垫圈8 | Seal washer8 | 2 | 易损件 EWP |
| 5 | Q1840816 | 螺栓M8×16 | Bolt M8× 16 | 3 |  |
| 6 | Q1840880TF2 | 螺栓M8×80 | Bolt M8× 80 | 4 |  |
| 7 | Q40108 | 垫圈8 | Nut 8 | 3 |  |
| 8 | Q40308 | 垫圈8 | Nut 8 | 3 |  |
| 9 | Q340B08 | 螺母M8 | Nut M8 | 3 |  |
| 10 | J56QA-1002250 | 喷油泵齿轮盖板 | Fuel injection pump gear cover | 1 |  |
| 11 | J5600-1002255 | 喷油泵齿轮盖板垫片 | Fuel injection pump gear cover gasket | 1 | 易损件 EWP |
| 12 | YC209-070090FR | 油封70×90 | Oil seal 70× 90 | 1 | 选装件 Optional |
|  | YC209-B070090PR | 油封70×90 | Oil seal 70× 90 | 1 | 选装件 Optional |
| 13 | Q1841450 | 螺栓M14×50 | Bolt M14× 50 | 2 |  |
| 14 | Q1840850TF2 | 螺栓M8×50 | Bolt M8× 50 | 4 |  |
| 15 | J5600-1002201A | 正时齿轮室 | Timing gear chamber | 1 |  |
| 16 | J5600-1002202 | 齿轮室垫片 | Gear cover washer | 1 | 易损件 EWP |
| 17 | Q/YC207-0816 | 螺栓 | Bolt | 3 |  |
| 18 | J5600-1002311 | 惰齿轮防磨板 | Idler gear wear plate | 1 |  |
| 19 | J5600-1002306 | 惰齿轮轴 | Idler gear shaft | 1 |  |
| 20 | Q5211230 | 销12×30 | Pin 12× 30 | 2 |  |
| 21 | Q150B0825TF2 | 螺栓M8×25 | Bolt M8× 25 | 6 |  |
| 22 | J5600-1002203A | 齿轮室盖板 | Gear housing cover plate | 1 |  |
| 23 | L3001-1002032 | 正时齿轮室垫片 | Timing gear spacer | 1 | 易损件 EWP |
| 24 | J5600-1002350 | 惰齿轮组件 | Idler gear assembly | 1 |  |
| 25 | Q1840825TF2 | 螺栓M8×25 | Bolt M8× 25 | 6 |  |
| 26 | J5600-1111304 | 接头 | Joint | 1 |  |
| 27 | YC208-B04250F | O形圈2.65×42.5 | O-ring 2.65× 42.5 | 1 | 易损件 EWP |
| 28 | Q1200885 | 螺柱M8×85 | Stud M8× 85 | 1 |  |
| 29 | Q1200875 | 螺柱M8×75 | Stud M8× 75 | 2 |  |
| 30 | Q1840880TF2 | 螺栓M8×80 | Bolt M8× 80 | 1 |  |
| 31 | L3000-1002084 | 空压泵惰齿轮座 | Air compressor idler gear seat | 1 |  |
| 32 | 231-1002083 | 惰齿轮衬套 | Idler gear bushing | 1 |  |
| 33 | A3000-1002042 | 空压机惰齿轮 | Air compressor idler gear | 1 |  |
| 34 | 231-1002087 | 惰齿轮减磨板 | Idler gear friction plate | 1 |  |
| 35 | Q1840820TF2 | 螺栓M8×20 | Bolt M8× 20 | 2 |  |
| 36 | YC208-B02000F | O形圈2.65×20 | O-ring 2.65× 20 | 1 | 易损件 EWP |
| 37 | A3000-1002085B | 惰齿轮座螺栓 | Idler gear seat bolt | 1 |  |

3图Drawing

3、J5600-1003000 气缸盖及气缸盖罩总成 Cylinder Head & Cylinder Head Cover Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | L3000-1007013 | 气门锁夹 | Valve lock clamp | 48 | 易损件 EWP |
| 2 | J5600-1003116 | 气门弹簧上座 | Valve spring upper seat | 24 | 易损件 EWP |
| 3 | J5600-1003106 | 气门弹簧 | Valve spring | 24 | 易损件 EWP |
| 4 | L3000-1003105SF1 | 气门杆油封 | Valve stem seal | 24 | 易损件 EWP |
| 5 | J5600-1003104 | 气门导管 | Valve guide pipe | 24 | 易损件 EWP |
| 6 | L3000-1003036A | 前吊耳 | Front lifter | 1 |  |
| 7 | Q1841225TF2 | 螺栓M12×25 | Bolt M12×25 | 5 |  |
| 8 | J5600-1003201 | 气缸盖罩垫片 | Cylinder head cover washer | 1 | 易损件 EWP |
| 9 | J5600-1003171A | 气缸盖 | Cylinder head | 1 |  |
| 10 | J5600-1003001 | 气缸盖垫片 | Cylinder head gasket | 1 | 易损件 EWP |
| 11 | J5600-1003173A | 进气门座圈 | Air intake valve seat ring | 12 | 易损件 EWP |
| 12 | J5600-1003111 | 进气门 | Intake valve | 12 | 易损件 EWP |
| 13 | J5600-1003174A | 排气门座圈 | Air Exhaust valve seat ring | 12 | 易损件 EWP |
| 14 | J5600-1003103 | 排气门 | Exhaust valve | 12 | 易损件 EWP |
| 15 | A30-1003035A | 缸盖短螺栓 | Cylinder head bolt (short) | 26 | 易损件 EWP |
| 16 | Q40306 | 垫圈 | Washer | 9 |  |
| 17 | Q150B0612 | 螺栓M6×12 | Bolt M6× 12 | 9 |  |
| 18 | Q72230 | 塞片30 | Spacer 30 | 14 |  |
| 19 | L3000-1003206 | 瓦塄钢丝团 | Steel wire roll | 1 |  |
| 20 | Q61904 | 螺塞NPT1/2 | Screw plug NPT 1/2 | 6 |  |
| 21 | L3000-1003151 | 后吊耳 | Rear lifter | 1 |  |
| 22 | J5600-1003270 | 盖板组件 | Cover part assembly | 1 |  |
| 23 | Q1840830 | 螺栓M8×30 | Bolt M8× 30 | 17 |  |
| 24 | J5600-1003205A | 气缸盖罩 | Cylinder head cover | 1 |  |
| 25 | J5600-1003248 | 加机油口垫片 | Oil filler washer | 1 | 易损件 EWP |
| 26 | Q1840816 | 螺栓M8×16 | Bolt M8× 16 | 4 |  |
| 27 | 150-1003043C | 密封圈 | Seal ring | 1 | 易损件 EWP |
| 28 | 150-1003041F | 加机油口盖 | Oil filler cover | 1 |  |
| 29 | J5600-1003243 | 加机油口 | Oil filler port | 1 |  |
| 30 | YC208-B02580F | O形圈2.65×25.8 | O-ring 2.65× 25.8 | 6 | 易损件 EWP |
| 31 | J5600-1003176 | 喷油器铜套 | Injector copper bushing | 6 |  |
| 32 | L3000-1003088 | 气缸盖定位销套 | Cylinder head dowel pin sleeve | 2 |  |

4图Drawing

4．J5600-1004000  活塞及连杆总成 Piston & Connecting Rod Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
|  | J5600-1004002* | 活塞环总成 | Piston ring assy | 6 | 包括1.2.3 Including Item 1, 2, 3 |
| 1 | J5600-1004002 | 气环 | Compression ring | 6 | 易损件 EWP |
| 2 | J5600-1004003 | 刮油环 | Oil control ring | 6 | 易损件 EWP |
| 3 | J5600-1004100 | 油环部件 | Oil control ring parts | 6 | 易损件 EWP |
| 4 | J5600-1004001SF3 | 活塞 | Piston | 6 | 易损件 EWP |
| 5 | A30-1004019 | 活塞销 | Piston pin | 6 |  |
| 6 | Q43040 | 挡圈40 | Retaining ring 40 | 12 | 易损件 EWP |
| 7 | A3000-1004202 | 连杆衬套 | Connecting rod bushing | 6 | 易损件 EWP |
|  | A3000-1004200 | 连杆部件 | Connecting rod components | 6 | 包括8.10.11 Including Item 8, 10, 11 |
| 8 | A3000-1004201 | 连杆体 | Connecting rod shank | 6 |  |
| 10 | A3000-1004203 | 连杆盖 | Connecting rod cap | 6 |  |
| 11 | 6105Q-1004054 | 连杆螺栓 | Connecting rod bolt | 12 | 易损件 EWP |
| 9 | A30-1004005 | 连杆轴瓦 | Connecting rod bearing shell | 6 | 易损件 EWP |

5图Drawing

5．J5600-1005000  曲轴减振器总成 Crankshaft Vibration Damper Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | Q150B1065TF2 | 螺栓M10×65 | Bolt M10× 65 | 4 |  |
| 2 | Q40110 | 垫圈10 | Washer 10 | 4 |  |
| 3 | Q40310 | 垫圈10 | Washer 10 | 4 |  |
| 4 | A4137-1005034A | 皮带轮压圈 | Belt pulley clamping ring | 1 |  |
| 5 | A3100-1005034A | 皮带轮螺栓 | Pulley bolt | 6 |  |
| 6 | A3100-1005032E | 皮带轮 | Pulley bolt | 1 |  |
| 7 | Q5210814 | 销8×14 | Pin 8× 14 | 1 |  |
| 8 | J5600-1005040A | 硅油减振器 | Silicone vibration damper | 1 |  |
| 9 | A3100-1005033 | 环垫 | Ring washer | 1 |  |
| 10 | Q218B1025TF2 | 螺钉M10×25 | Screw M10× 25 | 6 |  |
| 11 | A3100-1005021B | 曲轴正时齿轮 | Crankshaft timing gear | 1 |  |
| 12 | A3100-1005018 | 扁销 | Flat pin | 2 |  |
|  | 475D-1005054A*-L | 主轴瓦 | Main bearing shell | 1 | 包括13.17 |
| 13 | 475D-1005054A | 主轴瓦（上） | Main bearing shell (upper) | 7 |  |
| 17 | 475D-1005055A | 主轴瓦（下） | Main bearing shell (lower) | 7 |  |
| 14 | 6105Q-1005058A | 曲轴止推片 | Crankshaft thrust plate | 4 |  |
| 15 | J3600-1005015A | 曲轴 | Crankshaft | 1 |  |
| 16 | 6105Q-1005042 | 定位销 | Locating pin | 1 |  |

6图Drawing

6. J5600-1006000  凸轮轴总成  Camshaft Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | J5600-1006001B | 凸轮轴 | Camshaft | 1 |  |
| 2 | Q5500519 | 键5×19 | Pin 5×19 | 1 | 易损件 EWP |
| 3 | L3000-1006005A | 隔圈 | Spacer | 1 |  |
| 4 | L3000-1006003A | 凸轮轴止推垫片 | Camshaft thrust gasket | 1 |  |
| 5 | Q/YC207-0820 | 螺栓M8×20 | Bolt M8×20 | 2 |  |
| 6 | J5600-1006002 | 凸轮轴正时齿轮 | Camshaft timing gear | 1 |  |
| 7 | Q5210516 | 销5×16 | Pin 5× 16 | 1 |  |
| 8 | J5600-1006008D | 凸轮轴信号轮 | Camshaft signal panel | 1 |  |
| 9 | L3000-1006007 | 凸轮轴螺栓 | Camshaft bolt | 1 |  |

7图Drawing

7．J5600-1007000 配气机构总成 Valve Train Mechanism Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | L3000-1007027 | 定位套 | Locating liner | 2 | 易损件 EWP |
| 2 | L3000-1007025C | 摇臂座 | Rocker arm seat | 1 |  |
| 3 | Q5280612 | 销6×12 | Pin 6×12 | 2 | 易损件 EWP |
| 4 | YC208-A00500F | O形圈1.8×5 | O-ring 1.8×5 | 1 | 易损件 EWP |
| 5 | YC208-A00800F | O形圈1.8×8 | O-ring 1.8×8 | 1 | 易损件 EWP |
| 6 | L3000-1007070C | 球头结合件 | Ball-end united part | 2 |  |
| 7 | A3000-1007001 | 挺柱 | Tappet | 2 |  |
| 8 | L3000-1007028A | 气门桥 | Valve bridge | 2 |  |
| 9 | J5600-1007080 | 气门推杆组件 | Valve push rod parts | 2 |  |
| 10 | L3000-1007053 | 调整螺钉 | Adjusting bolt | 2 |  |
| 11 | L3000-1007062C | 气门摇臂衬套 | Valve rocker arm bushing | 2 | 易损件 EWP |
| 12 | L3000-1007061A | 气门摇臂 | Valve rocker arm | 2 |  |
| 13 | 6105Q-1007054 | 锁紧螺母 | Lock nut | 2 |  |
| 14 | Q/YC207-1075 | 螺栓 | Bolt | 3 |  |
| 15 | Q1840835TF2 | 螺栓M8×35 | Bolt M8×35 | 2 |  |
| 16 | L3000-1007026C | 摇臂轴 | Rocker arm | 1 |  |

8图Drawing

8．J5600-1008100  进气管部件 Intake Manifold Parts

J5600-1008500  进气接管部件 Air Intake Pipe Parts

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | J5600-1008101C | 进气管 | Intake manifold | 1 |  |
| 2 | Q1841090 | 螺栓M10×90 | Bolt M10×90 | 8 |  |
| 3 | Q18410100 | 螺栓M10×100 | Bolt M10×100 | 12 |  |
| 4 | Q1841065 | 螺栓M10×65 | Bolt M10×65 | 4 |  |
| 5 | J5600-1008104 | 进气管垫片 | Intake manifold spacer | 4 | 易损件 EWP |
| 6 | J5600-1008105A | 进气接管垫片 | Intake manifold spacer | 1 | 易损件 EWP |
| 7 | Q1201035 | 螺柱M10×35 | Stud M10×35 | 4 |  |
| 8 | Q40110 | 垫圈10 | Washer 10 | 4 |  |
| 9 | Q40310 | 垫圈10 | Washer 10 | 4 |  |
| 10 | Q340B10 | 螺母M10 | Nut M10 | 4 |  |
| 11 | Q/YC198-20 | 螺塞M20×1.5 | Screw plug M20×1.5 | 3 |  |
| 12 | Q/YC149-20 | 复合式密封垫圈20 | Combined seal washer 20 | 3 |  |
| 13 | J5600-1008102A | 进气接管 | Air intake pipe | 1 |  |

9图Drawing

9．J5600-1008200  排气管部件 E× haust Manifold Parts

J5600-1008400  排气管护罩部件 Manifold Cover Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | J5600-1008250 | 排气管垫片组件 | Exhaust manifold gasket parts | 6 | 易损件 EWP |
| 2 | J5600-1008217A | 排气支管 | Exhaust manifold | 2 |  |
| 3 | J5600-1008026 | 螺栓套 | Bolt sleeve | 22 |  |
| 4 | Q150B1075TF2 | 螺栓M10×75 | Bolt 10×75 | 22 |  |
| 5 | J5600-1008211 | 排气管罩 | Exhaust manifold cover | 1 |  |
| 6 | Q1841016 | 螺栓M10×16 | Bolt M10×16 | 1 |  |
| 7 | Q1840815 | 螺栓M8×15 | Bolt M8×25 | 6 |  |
| 8 | Q1841025TF2 | 螺栓M10×25 | Bolt M10×25 | 2 |  |
| 9 | J62AA-1008218AL | 排气中间管 | Exhaust middle pipe | 1 |  |
| 10 | L3000-1008025 | 密封环 | Seal ring | 4 |  |

10图Drawing

10.   J5600-1009000    油底壳总成 Oil Sump Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | J56QA-1009040 | 油底壳组件 | Oil sump parts | 1 |  |
| 2 | 6105Q-1009032A | 放油塞磁铁 | Oil drain plug magnet | 1 |  |
| 3 | 6105Q-1009031C | 放油塞 | Oil drain plug | 1 |  |
| 4 | Q/YC149-27 | 复合式密封垫圈27 | Seal washer 27 | 1 | 易损件 EWP |
| 5 | M3000-1009002 | 油底壳压块 | Oil sump press block | 10 |  |
| 6 | Q1840840 | 螺栓M8×40 | Bolt M8× 40 | 11 |  |
| 7 | L3000-1009002 | 油底壳压块 | Oil sump press block | 2 |  |
| 8 | J5600-1009002 | 油底壳压块 | Oil sump press block | 1 |  |
| 9 | L3000-1009001 | 油底壳垫 | Oil sump washer | 1 | 易损件 EWP |
| 10 | Q1840865TF2 | 螺栓M8×65 | Bolt M8×65 | 2 |  |

11图Drawing

11.  J5600 -1010000  机油集滤器总成 Oil Strainer Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | 6105QA-1010130B | 滤网总成 | Filter screen assembly | 1 |  |
| 2 | J56QA-1010100 | 吸油管部件 | Oil suction parts | 1 |  |
| 3 | Q150B0816TF2 | 螺栓M8×16 | Bolt M8×16 | 1 |  |
| 4 | Q40308 | 垫圈8 | Washer 8 | 1 |  |
| 5 | Q40108 | 垫圈8 | Washer 8 | 1 |  |
| 6 | Q218B0875TF2 | 螺钉M8×75 | Screw M8×75 | 2 |  |
| 7 | 6105QA-1010110 | 垫片结合件 | Washer united part | 1 | 易损件 EWP |

12图Drawing

12.  J5600-1011000  机油泵总成 Oil Pump Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
|  | A30-1011020A | 机油泵 | Oil pump | 1 | 包括1-9,14-19 Including item 1-9, 14-19 |
| 1 | A30-1011023 | 机油泵齿轮 | Oil pump gear | 1 |  |
| 2 | A30-1011024A | 机油泵盖 | Oil pump cover | 1 |  |
| 3 | A30-1011022 | 机油泵驱动齿轮 | Oil pump driving gear | 2 |  |
| 4 | Q5210412 | 圆柱销4×12 | Column pin 4×12 | 2 |  |
| 5 | A30-1011021A | 机油泵体 | Oil pump body | 1 |  |
| 6 | Q150B1050TF2 | 螺栓M10×50 | Bolt M10×50 | 2 |  |
| 7 | Q40310 | 垫圈10 | Washer 10 | 3 |  |
| 8 | Q40110 | 垫圈10 | Washer 10 | 3 |  |
| 9 | A30-1011026 | 机油泵从动齿轮轴 | Oil pump driven gear shaft | 1 |  |
| 10 | J5600-1011240A | 出油管组件 | Oil outlet pipe assembly | 1 |  |
| 11 | Q218B0825TF2 | 螺钉M8×25 | Screw M8×25 | 4 |  |
| 12 | Q40308 | 垫圈8 | Washer 8 | 4 |  |
| 13 | 6105QA-1010110 | 垫片结合件 | Assembled washer | 2 | 易损件 EWP |
| 14 | A30-1011025 | 机油泵驱动齿轮轴 | Oil pump drive gear shaft | 1 |  |
| 15 | Q150B0860 | 螺栓M8×60 | Bolt M8×60 | 4 |  |
| 16 | Q5280532 | 销5×32 | Pin 5×32 | 1 |  |
| 17 | A30-1011028 | 机油泵限压阀塞 | Oil pump relief valve plug | 1 |  |
| 18 | A30-1011029 | 机油泵限压阀弹簧 | Oil pump relief valve spring | 1 |  |
| 19 | A30-1011031 | 挡圈 | Retainer | 1 |  |
| 20 | Q351B10 | 螺母M10×1 | Nut M10×1 | 1 |  |
| 21 | 430-1011012 | 间隔垫 | Spacer | 1 |  |
| 22 | 430-1011011 | 机油泵中间驱动齿轮 | Oil pump middle driving gear | 1 |  |
| 23 | Q43040 | 挡圈40 | Retaining ring 40 | 1 |  |
| 24 | GB/T276-6203 | 滚动轴承6203 | Rolling bearing 6203 | 2 |  |
| 25 | 430-1011014 | 垫圈-中间传动齿轮 | Spacer- driven gear | 1 |  |
| 26 | A30-1011013 | 机油泵中间传动齿轮轴 | Oil pump middle driving gear shaft | 1 |  |

13图Drawing

13．A3100-1012000机油滤清器总成 Oil Filter Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | 430-1012020A | 机油滤清器 | Oil filter | 1 |  |

14图Drawing

14、A3100-1013000A 机油冷却器总成 Oil Cooler Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | A3100-1013001A | 机油冷却器垫片 | Oil cooler spacer | 1 |  |
|  | A3100-1013010D | 机油冷却器 | Oil cooler | 1 | 包括2-12 Including item 2-12 |
| 2 | A3000-1013020 | 机油冷却器芯 | Oil cooler core | 1 |  |
| 3 | A3100-1013011D | 机油冷却器盖 | Oil cooler cover | 1 |  |
| 4 | Q1840875TF2 | 螺栓M8×75 | Bolt M8× 75 | 7 |  |
| 5 | Q1840880TF2 | 螺栓M8×80 | Bolt M8× 80 | 3 |  |
| 6 | Q1840825TF2 | 螺栓M8×25 | Bolt M8× 25 | 14 |  |
| 7 | Q1840855 | 螺栓M8×55 | BoltM8× 55 | 2 |  |
| 8 | Q1841425 | 螺栓M14×25 | Bolt M14× 25 | 1 |  |
| 9 | Q18408110 | 螺栓M8×110 | Bolt M8× 110 | 1 |  |
| 10 | 475D-1002071A | 回油接头 | Oil return union bolt | 1 |  |
| 11 | Q1840850 | 螺栓M8×50 | Bolt M8× 50 | 7 |  |
| 12 | Q1840820 | 螺栓M8×20 | Bolt M8× 20 | 4 |  |

15图Drawing

15. J5600-1014000曲轴箱通风装置总成 Crankcase Ventilation Device Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | Q67645 | 环箍45 | Ring hoop 45 | 2 |  |
| 2 | J5600-1014049A | 通气管Ⅰ | Ventilation pipe Ⅰ | 1 |  |
| 3 | J5600-1014100A | 离心式油气分离器 | centrifugal type oil-air separator | 1 |  |
| 4 | Q1841016 | 螺栓M10×16 | Bolt M10× 16 | 2 |  |
| 5 | G2000-1014009 | 回油胶管 | Oil return rubber pipe | 1 |  |
| 6 | Q67627 | 环箍27 | Ring hoop 27 | 2 |  |
| 7 | J6000-1014028A | 回油管 | Oil return pipe | 1 |  |

16图Drawing

16.  J5600-1028000  油标尺总成 Dipstick Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | L3002-1009080B | 油标尺焊接件 | Oil dipstick weldment | 1 |  |
| 2 | 151-1002082 | 油标尺管夹 | Oil dipstick pipe clamp | 1 |  |
| 3 | 173A-1009041 | 软管 | Hose | 1 |  |
| 4 | J5600-1009009 | 油标尺支撑板 | Oil dipstick support plate | 1 |  |
| 5 | Q1840825 | 螺栓M8×25 | Bolt M8× 25 | 1 |  |
| 6 | Q340B08 | 螺母M8 | Nut M8 | 1 |  |

17图Drawing

17．J5600-1104000  供给系管路总成 Fuel Supply Lines Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | L3000-1104131 | 连接管螺栓 | Connecting pipe bolt | 6 |  |
| 2 | G2100-1104050A | 高压连接管组件 | High pressure connecting pipe assembly | 6 |  |
| 3 | J5600-1104100A | 高压油管部件 | High pressure pipe parts | 1 | 易损件 EWP |
| 4 | Q/YC901-1C12125 | 铰接螺栓M12×1.25 | Articulated bolt M12×1.25 | 2 |  |
| 5 | Q/YC149-12 | 复合式密封垫圈12 | Seal ring washer 12 | 4 | 易损件 EWP |
| 6 | J5600-1104C00BSF1 | 共轨管回油管部件 | CR(Common rail) oil return pipe parts | 1 | 易损件 EWP |
| 7 | J5600-1104200E | 回油管部件 | Oil return pipe parts | 1 | 易损件 EWP |
| 8 | J5600-1104260 | 回油管管夹支架组件 | Oil return pipe clamp bracket assembly | 1 |  |
| 9 | J5600-1104900B | 进油管部件 | Oil inlet pipe parts | 1 | 易损件 EWP |
| 10 | Q/YC149-16 | 复合式密封垫圈16 | Seal ring washer 16 | 8 | 易损件 EWP |
| 11 | Q/YC901-1C1615 | 铰接螺栓M16×1.5 | Hinged bolt M16×1.5 | 2 |  |
| 12 | J5600-1104504B | 燃油分配器支架 | Fuel distributor bracket | 1 |  |
| 13 | Q1841025TF2 | 螺栓M10×25 | Bolt M10×25 | 4 |  |
| 14 | J5600-1104541A | 燃油分配器 | Fuel distributor | 1 |  |
| 15 | G5800-1104001 | 过渡接头 | Transit joint | 4 |  |
| 16 | Q1840825TF2 | 螺栓M8×25 | Bolt M8×25 | 1 |  |
| 17 | Q/YC149-10 | 复合式密封垫圈10 | Seal washer 10 | 2 | 易损件 EWP |
| 18 | M3000-1002701A | 过油螺栓 | Bolt with oil hole | 1 |  |
| 19 | J5600-1104F00ASF1 | ECU至输油泵油管部件 | Pipe parts, ECU to fuel pump pipe | 1 |  |
| 20 | J5600-1104A00SF1 | 燃油分配器至喷油泵油管部件 | Pipe parts, fuel distributor to injection pump | 1 | 易损件 EWP |
| 21 | J5600-1104400BSF2 | 柴滤器至喷油泵油管部件 | Pipe parts, fuel filter to injection pump | 1 | 易损件 EWP |
| 22 | J5600-1104300BSF2 | 输油泵至柴滤器油管部件 | Pipe parts, fuel pump to filter | 1 | 易损件 EWP |
| 23 | J5600-1104C10 | 管夹支架组件 | Pipe clamp bracket assembly | 1 |  |
| 24 | J5600-1104080ASF1 | 油泵至油轨油管部件 | Pipe parts, oil pump to oil rail pipe | 1 | 易损件 EWP |
| 25 | J5600-1104205 | 接头 | Joint | 6 |  |
| 26 | Q/YC149-8 | 复合式密封垫圈8 | Combined seal washer 8 | 12 | 易损件 EWP |

18图Drawing

18．J5600-1105000  柴油滤清器总成 Fuel Filter Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | G5800-1105001A | 柴油滤清器座 | Fuel filter seat | 1 |  |
| 2 | Q/YC149-16 | 复合式密封垫圈16 | Seal ring washer 16 | 4 | 易损件 EWP |
| 3 | Q/YC901-1C1615 | 铰接螺栓M16×1.5 | Articulated bolt M16×1.5 | 2 |  |
| 4 | Q1841025 | 螺栓M10×25 | Bolt M10×25 | 2 |  |
| 5 | Q40310 | 垫圈10 | Washer 10 | 2 |  |
| 6 | Q40110 | 垫圈10 | Washer 10 | 2 |  |
| 7 | G5800-1105140 | 滤芯组件 | Filter core assembly | 1 | 易损件 EWP |
| 8 | G5800-1105240 | 预滤组件 | Pre-filter assembly | 1 |  |
| 9 | G5800-1105210 | 滤座组件 | Filter seat assembly | 1 |  |

19图Drawing

19．J5600-1111000 喷油泵总成 Injection Pump Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | J5600-1111003 | 燃油喷射泵齿轮 | Fuel injection pump gear | 1 |  |
| 2 | J5600-1111001 | 燃油喷射泵连接盘 | Fuel injection pump connecting pan | 1 |  |
| 3 | YC208-B05600F | O形圈2.65×56 | O-ring 2.65× 56 | 1 | 易损件 EWP |
| 4 | G2100-1111100-A38 | 燃油喷射泵部件 | Fuel injection pump parts | 1 |  |
| 5 | Q/YC149-8 | 复合式密封垫圈8 | Seal washer8 | 3 | 易损件 EWP |
| 6 | Q1840845TF2 | 螺栓M8×45 | Bolt M8× 45 | 3 |  |
| 7 | J5600-1111A00 | 共轨管部件 | Common rail pipe parts | 1 |  |
| 8 | Q1840820TF2 | 螺栓M8×20 | Bolt M8× 20 | 3 |  |

20图Drawing

20.  J5600-1112000  喷油器总成 Injector Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | J5600-1112001ASF1 | 喷油器垫片 | Injector gasket | some | 易损件 EWP |
| 2 | J5600-1112100-A38 | 喷油器部件 | Injector parts | 6 |  |
| 3 | J5600-1112003 | 螺柱 | Stud | 6 |  |
| 4 | J5600-1112005D | 固定板 | Lock plate | 6 |  |
| 5 | J5600-1112002 | 垫圈 | Washer | 6 |  |
| 6 | J5600-1112008 | 螺母 | Nut | 6 |  |

21图Drawing

21．J5600-1118000  增压器总成 Turbocharger Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | Q150B0825TF2 | 螺栓M8×25 | Bolt M8×25 | 4 |  |
| 2 | Q40308 | 垫圈8 | Washer 8 | 4 |  |
| 3 | 475D-1118022 | 法兰压板 | Flange | 1 |  |
| 4 | 475D-1118021 | 增压器进油接头 | Turbocharger oil inlet joint | 1 |  |
| 5 | 150-1118031B | 垫片 | Washer | 1 | 易损件 EWP |
| 6 | J5600-1118100-135 | 增压器 | Turbocharger | 1 | 选装件 Optional |
| 7 | B3000-1118041 | 垫片 | Washer | 1 | 易损件 EWP |
| 8 | 6105Q-3509013 | 垫圈 | Washer | 2 |  |
| 9 | M3000-1008206A | 螺母 | Nut | 4 |  |
| 10 | Q40110 | 垫圈10 | Washer 10 | 4 |  |
| 11 | L3000-1118002 | 增压器垫片 | Turbocharger gasket | 1 |  |
| 12 | L3000-1118011 | 双头螺柱 | Stud | 4 |  |
| 13 | L3002-1118340B | 增压器回油管 | Turbocharger oil return pipe | 1 |  |
| 14 | YC208-B01700F | O形圈2.65×17 | O-ring 2.65×17 | 2 | 易损件 EWP |
| 15 | J5600-1008203 | 涡轮后排气接管 | Turbine rear Exhaust pipe | 0 |  |
| 16 | J5600-1008212 | 支架 | Bracket | 0 |  |
| 17 | Q1841020 | 螺栓M10×20 | Bracket | 0 |  |
| 18 | Q340B10 | 螺母M10 | Nut M10 | 0 |  |
| 19 | Q40310 | 垫圈10 | Lock Washer 10 | 0 |  |
| 20 | G0100-1118072C | 涡轮后卡环 | Turbine rear circlip | 2 |  |
| 21 | G0100-1118073A | 垫片 | Washer | 1 | 易损件 EWP |
| 22 | Q/YC149-14 | 复合式密封垫圈14 | Seal washer 14 | 1 | 易损件 EWP |
| 23 | A30-1118021 | 进油软管接头 | Oil intake hose joint | 1 |  |
| 24 | Q150B1035 | 螺栓M10×35 | Bolt M10×35 | 2 |  |
| 25 | B4000-1118030 | 增压器进油软管 | Turbocharger oil inlet hose | 1 |  |

22图Drawing

22.    631-1305000 放水开关总成 Water Drain Cock Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | 6105Q-1305010 | 放水阀部件 | Water drain cock parts | 1 |  |
| 2 | Q5003225 | 销3.2×25 | Pin 3.2× 25 | 1 |  |
| 3 | 150-1305015 | 操纵杆 | Control handle | 1 |  |

23图Drawing

23．J5600-1306000 调温器总成 Thermostat Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | Q618B02 | 螺塞NPT1/4 | Screw plug NPT1/4 | 1 |  |
| 2 | Q340B08 | 螺母M8 | Nut M8 | 6 |  |
| 3 | Q40308 | 垫圈8 | Washer 8 | 6 |  |
| 4 | Q40108 | 垫圈8 | Washer 8 | 6 |  |
| 5 | Q1200825 | 螺柱M8×25 | Stud M8× 25 | 6 |  |
| 6 | 156-1306012 | 调温器盖 | Thermostat cover | 1 |  |
| 7 | A3900-1303012 | 节温器盖垫片 | Thermostat cover spacer | 1 | 易损件 EWP |
| 8 | M7600-1306004 | 调温器 | Thermostat | 2 |  |
| 9 | J5600-1306003E | 调温器座 | Thermostat seat | 1 |  |
| 10 | YC208-C03550 | O形圈3.55×35.5 | O-ring 3.55× 35.5 | 1 | 易损件 EWP |
| 11 | 177-1306023C | 螺塞 | Bolt plug | 1 |  |
| 12 | Q618B03 | 螺塞NPT3/8 | Screw plug NPT3/8 | 1 |  |
| 13 | Q1840870TF2 | 螺栓M8×70 | Bolt M8× 70 | 2 |  |
| 14 | Q618B04 | 螺塞NPT1/2 | Screw plug NPT1/2 | 1 |  |
| 15 | Q1840845TF2 | 螺栓M8×45 | Bolt M8× 45 | 2 |  |
| 16 | J5600-1306005 | 回水胶管 | Water return rubber pipe | 1 | 易损件 EWP |
| 17 | Q67650 | 环箍50 | Ring hoop 50 | 2 | 易损件 EWP |
| 18 | J5600-1306006A | 节温器座垫片 | Thermostat seat washer | 1 | 易损件 EWP |

24图Drawing

24．J5600-1307000    水泵总成 Water Pump Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | A3100-1307004B | 水泵垫片(II) | Water pump washer (II) | 1 | 易损件 EWP |
| 2 | A3100-1307010B | 水泵部件 | Water pump part | 1 |  |
| 3 | Q1841075TF2 | 螺栓M10×75 | Bolt M10× 75 | 3 |  |
| 4 | Q1841065TF2 | 螺栓M10×65 | Bolt M10× 65 | 2 |  |

25图Drawing

25．A3100-1308000   风扇总成 Fan Parts

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | G3202-1308010B | 硅油离合器风扇组件 | Silicon oil clutch fan assembly | 0 |  |
| 2 | Q1841230TF2 | 螺栓M12×30 | Bolt M12× 30 | 0 |  |

26图Drawing

26.   J5600-1600000 动力输出总成 Power Output Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | A3200-1600401A | 飞轮壳 | Flywheel housing | 1 |  |
| 2 | 6105Q-1600011 | 扁销 | Flat pin | 1 |  |
| 3 | Q40314 | 垫圈14 | Washer 14 | 2 |  |
| 4 | Q150B1450TF2 | 螺栓M14×50 | Bolt M14×50 | 2 |  |
| 5 | 150-1002062 | 曲轴后油封 | Crankshaft rear oil seal | 1 | 易损件 EWP |
|  | A3206-1005360 | 飞轮及齿圈组件 | Flywheel and geared ring | 1 | 包括6.7 Including item 6, 7 |
| 6 | A3206-1005361 | 飞轮 | Flywheel | 1 |  |
| 7 | A3206-1005362 | 齿圈 | Gear circle | 1 |  |
| 8 | GB/T276-6205-2RS | 深沟球轴承 | Ball bearing | 1 | 易损件 EWP |
| 9 | 397A-1600050 | 轴承衬垫 | Bearing bushing | 1 |  |
| 10 | 6QA1-1005044A | 飞轮螺栓 | Flywheel bolt | 8 |  |
| 11 | Q5221224 | 销12×24 | Pin 12×24 | 1 |  |
| 12 | Q150B1250TF2 | 螺栓M12×50 | Bolt M12×50 | 6 |  |
| 13 | Q40312 | 垫圈12 | Washer 12 | 8 |  |
| 14 | Q150B1240TF2 | 螺栓M12×40 | Bolt M12×40 | 2 |  |
| 15 | Q40106 | 垫圈6 | Washer 6 | 4 |  |
| 16 | Q40306 | 垫圈6 | Washer 6 | 4 |  |
| 17 | Q150B0616 | 螺栓M6×16 | Bolt M6×16 | 4 |  |
| 18 | B3000-1600021 | 盖板 | Cover plate | 1 |  |
| 19 | Q/YC198-18 | 螺塞M18×1.5 | Screw plug M18×1.5 | 1 |  |
| 20 | 330-1600016 | 离合器壳垫片 | Clutch housing gasket | 1 | 易损件 EWP |

27图Drawing

27．A3000-3407000  转向泵总成 Steering Pump Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | A3007-3407100 | 转向泵 | Steering pump | 1 | 选装件 Optional |
| 2 | Q40110 | 垫圈10 | Washer 10 | 2 |  |
| 3 | Q40310 | 垫圈10 | Washer 10 | 2 |  |
| 4 | Q150B1035 | 螺栓M10×35 | Bolt M10×35 | 2 |  |
| 5 | B3430-3407004 | 转向泵出油接头 | Steering pump oil out let joint | 0 |  |
| 6 | YC208-M01600F | O型圈2.4×16 | O-ring 2.4×16 | 0 | 易损件 EWP |
| 7 | YC208-B05800F | O型圈2.65×58 | O-ring 2.65×58 | 1 | 易损件，随泵带来 EWP, with the pump |
| 8 | 231-3407013 | 传动套 | Driving sleeve | 1 |  |

28图Drawing

28.  J6000--3509000  气制动空气压缩机总成 Pneumatic Air Compressor Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | 6QA6-1307017 | 过水螺栓 | Bolt with water hole | 4 |  |
| 2 | Q/YC149-14 | 复合式密封垫圈14 | Seal washer 14 | 8 | 易损件 EWP |
| 3 | A3000-3509024 | 空压机回水管组件 | Air compressor backwater pipe assembly | 1 |  |
| 4 | A440B-3509100 | 空气压缩机 | Air compressor | 1 |  |
| 5 | A3100-3509005 | 空压机进水管 | Water inlet pipe, air compressor | 1 |  |
| 6 | L3000-3509009 | 空压机垫片 | Air compressor gasket | 1 | 易损件 EWP |
| 7 | A3000-3509018 | 空压机齿轮 | Air compressor gear | 1 |  |
| 8 | Q150B1085 | 螺栓M10×85 | Bolt M10× 85 | 1 |  |
| 9 | Q150B1040 | 螺栓M10×40 | Bolt M10× 40 | 2 |  |
| 10 | Q40310 | 垫圈10 | Washer 10 | 3 |  |
| 11 | Q340B10 | 螺母M10 | Nut M10 | 3 |  |
| 12 | A3515-3509240 | 空压机进油管组件 | Oil intake pipe assy. of air compressor | 1 |  |
| 13 | M3000-1002701A | 过油螺栓 | Bolt with oil hole | 3 |  |
| 14 | Q/YC149-10 | 复合式密封垫圈10 | Seal washer 10 | 6 | 易损件 EWP |

29图Drawing

29、J5600-3701000 发电机总成 Alternator Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | Q340B10 | 螺母M10 | Nut M10 | 2 |  |
| 2 | Q40310 | 垫圈10 | Washer 10 | 2 |  |
| 3 | Q40110 | 垫圈10 | Washer 10 | 2 |  |
| 4 | A3008-3701032 | 发电机调节板 | Alternator adjusting plate | 0 |  |
| 5 | Q340B08 | 螺母M8 | Nut M8 | 1 |  |
| 6 | Q40308 | 垫圈8 | Washer 8 | 1 |  |
| 7 | Q40108 | 垫圈8 | Washer 8 | 1 |  |
| 8 | A3100-3701100A | 充电发电机 | Alternator | 0 |  |
| 9 | Q1840835 | 螺栓M8×35 | Bolt M8× 35 | 2 |  |
| 10 | Q1840820 | 螺栓M8×20 | Bolt M8× 20 | 2 |  |
| 11 | J56QA-3701002 | 发电机支架 | Alternator bracket | 1 |  |
| 12 | B4000-1307042 | 多锲带 | Multi-wedge belt | 1 | 易损件 EWP |
| 13 | Q150B10130 | 螺栓M10×130 | Bolt M10× 130 | 1 |  |
| 14 | Q1840855 | 螺栓M8×55 | Bolt M8× 55 | 1 |  |
| 15 | Q150B1045 | 螺栓M10×45 | Bolt M10× 45 | 1 |  |

30图Drawing

30. A3206-3708000 起动机总成 Starter Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | A70-3708010B | 起动机 | Starter | 1 |  |
| 2 | G0202-3708020 | 起动机垫块 | Starter spacer | 1 |  |
| 3 | Q150B1240 | 螺栓M12×40 | Bolt M12×40 | 3 |  |
| 4 | Q40312 | 垫圈12 | Washer 12 | 3 |  |
| 5 | A3206-3708104 | 起动机防护罩 | Starter protection cover | 1 |  |

31图Drawing

31.  1532-3800000 仪表、感应器总成 Sensors

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | 365C-3800030 | 油压感应塞 | Oil pressure sensor | 0 |  |

32图Drawing

32、J5600-3823000 控制系统总成 Control System Assembly

| 序号 Item | 图 号 Part No. | 名 称 | Name | 数量 Qty. | 备 注 Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | G2100-3823344 | ECU减震垫 | ECU vibration damper | 8 | 易损件 EWP |
| 2 | Q1841035 | 螺栓M10×35 | Bolt M10× 35 | 4 |  |
| 3 | J5600-3823021 | 主线束支架(I) | Main wire harness bracket（I） | 1 |  |
| 4 | J5600-3823220 | 发动机线束组件 | Engine wire harness assembly | 1 |  |
| 5 | J5600-3823031 | 支线束支架(I) | Branch wire harness bracket （I） | 5 |  |
| 6 | G6000-3823353 | 机型软件标签 | Model software label | 1 | 易损件 EWP |
| 7 | G2100-3823351 | 控制器 | Controller | 1 |  |
| 8 | Q1840630 | 螺栓M6×30 | Bolt M6× 30 | 8 |  |
| 9 | G2100-3823341A | 冷却器盒 | Cooler housing | 1 |  |
| 10 | Q1840615 | 螺栓M6×15 | Bolt M6× 15 | 3 |  |
| 11 | G2100-3823140 | 增压压力及温度传感器 | Turbocharger pressure and temperature sensor | 1 |  |
| 12 | J5600-3823007A | 喷油控制线束支架 | Injection control harness bracket | 1 |  |
| 13 | J5600-3823210 | 喷油器线束组件 | Injector harness assembly | 1 |  |
| 14 | G2100-3823180 | 水温传感器 | Engine coolant temperature sensor | 1 |  |
| 15 | G2100-3823170 | 曲轴转速传感器 | Crankshaft speed sensor | 2 |  |
| 16 | Q40208 | 垫圈8 | Washer 8 | 2 |  |
| 17 | Q40308 | 垫圈8 | Washer 8 | 2 |  |
| 18 | Q1200818 | 螺柱M8×18 | Stud M8× 18 | 2 |  |
| 19 | Q340B08 | 螺母M8 | Nut M8 | 2 |  |
| 20 | J5600-3800301A | 转速传感器支架 | Speed sensor bracket | 1 |  |
| 21 | J5600-3800302 | 传感器支架定位螺套 | Sensor bracket positioning screw sleeve | 2 |  |